The purpose of this checklist is to provide useful information for the compliance of Categories 1B and 2 Construction Projects within the City and County of Honolulu with storm water erosion and sediment control guidelines, and incorporates Rules Relating to Water Quality requirements (effective December 24, 2018).

This checklist is not intended to summarize, supersede or contradict the regulations; please refer to the rules for a complete listing of requirements.

| Project Name: |  |
| --- | --- |
| Project Location: |  |
| Tax Map Key: |  |

| Disturbed Area (acres or square feet): |  |
| --- | --- |

| Categories 1B and 2 ESCP Requirements |
| --- |
| The following site features have been included on the plans: |
|  | Vicinity map showing the location of streams, channels, and drainage structures located within 50 feet of the Project Site |
|  | BMP Site Plan, which depicts the outline of buildings and structures, provides a clear delineation of disturbed areas, and the proximate location of proposed BMPs |
| Erosion Control BMPs |
|  | Project Planning and Design |
|  | Project Scheduling |
|  | Slope Management and Protection |
|  | Temporary Stabilization |
|  | Permanent Stabilization |
| Sediment Control BMPs |
|  | Storm Drain Inlet Protection |
|  | Perimeter Controls |
| Good Housekeeping BMPs |
|  | BMP and Site Maintenance |
|  | Dust Control |
|  | Material Delivery, Storage and Use BMPs |
|  | Stockpile Management BMPs |
|  | Spill Prevention and Control BMPs |
|  | Solid Waste Management BMPs |
|  | Hazardous Waste Management BMPs |
| Good Housekeeping BMPs (continued) |
|  | Contaminated Soil Management BMPs |
|  | Concrete Waste Management BMPs |
|  | Sanitary/Septic Waste Management BMPs |
|  | Liquid Waste Management BMPs |
|  | Vehicle and Equipment Cleaning BMPs |
|  | Vehicle and Equipment Fueling BMPs |
|  | Vehicle and Equipment Maintenance BMPs |
|  | Tracking Control |
| Erosion and Sediment Control Notes |
|  | DPP’s Construction BMP Standard Details |
|  | If any of the BMPs listed above are not included in an ESCP for a Category 1B or 2 Project, the ESCP Notes shall provide a list of the omitted BMPs with a brief explanation of why each omitted BMP is unnecessary or impracticable for the project |
| The following inspection notes have been included under the “Project Sequence” heading: |
|  | Inspection frequency: Once every 30 days If the project will be completed in less than thirty days, inspection shall occur midway through the project |
|  | Inspector must complete a report within 48 hours of an inspection Use DPP’s Appendix C – Construction Site BMPs Inspection Checklist for CCH Category 1A, 1B, 2, 3, and 4 and Trenching Projects Maintain all inspection reports and photographs in a “Project Log” |
| Changes to the ESCP *for changes to the ESCP after DPP’s initial plan review |
|  | Minor changes should be noted on the site copy of the ESCP and initialed by a DPP inspector |
|  | Major changes must be proposed to the Director in writing and approved before work resumes |
| ESCP Coordinator Information |
| Designating an ESCP Coordinator: |
|  | Use DPP’s Appendix B - Erosion and Sediment Control Plan Small Project Template, and have it signed by the Property Owner or Authorized Agent |
|  | A certified ESCP Coordinator must be designated with the original plan submittal; however the coordinator may be changed/updated at any time using DPP’s Appendix A or B |
|  | Changes to the ESCP Coordinator must be submitted to DPP in writing immediately for acceptance |