The purpose of this checklist is to provide useful information for the compliance of Category 4 Construction Projects within the City and County of Honolulu with storm water erosion and sediment control guidelines, and incorporates Rules Relating to Water Quality requirements (effective December 24, 2018).

This checklist is not intended to summarize, supersede or contradict the regulations; please refer to the rules for a complete listing of requirements.

| Project Name: |  |
| --- | --- |
| Project Location: |  |
| Tax Map Key: |  |

| Disturbed Area (acres or square feet): |  |
| --- | --- |

| Category 4 ESCP Requirements |
| --- |
|  | Prepared by a Certified ESCP Preparer when training becomes available; in the interim, a Hawaii-licensed Civil Engineer |
| The following site features have been included on the plans: |
|  | Location map showing the name, coordinates, and classification (e.g., Class 1, 2, Class A, Class AA waters) of State Receiving Waters |
|  | Vicinity map showing the location of streams, channels, and drainage structures located within 100 feet of the Project Site |
|  | Location of the 100-year flood plain |
|  | Existing and finished contours of the site |
|  | Existing and final drainage patterns and discharge points |
|  | Proposed structures, impervious areas, existing vegetation, final landscaping conditions, and appurtenant improvements |
|  | Erosion control notes including non-structural BMPs |
|  | BMP Site Plan, drawn to scale, which depicts the outline of buildings and structures, provides a clear delineation of disturbed areas, and the proximate location of proposed BMPs |
|  | BMP design details and notes clearly identifying temporary BMPs, permanent BMPs, a schedule for BMP implementation, and BMP maintenance activities |
|  | List or table of preconstruction, during construction, and post construction BMPs |
|  | Any additional information required by the director |
| Erosion Control BMPs |
|  | Project Planning and Design |
|  | Project Scheduling |
|  | Slope Management and Protection |
| Erosion Control BMPs (continued) |
|  | Permanent Stabilization |
|  | Temporary Stabilization |
|  | Diversion BMPs to divert runoff from upstream areas around disturbed areas of the Site |
|  | Velocity Dissipation Devices |
| Sediment Control BMPs |
|  | Storm Drain Inlet Protection |
|  | Perimeter Controls |
|  | Sediment Barriers |
| Good Housekeeping BMPs |
|  | BMP and Site Maintenance |
|  | Dust Control |
|  | Material Delivery, Storage and Use BMPs |
|  | Stockpile Management BMPs |
|  | Spill Prevention and Control BMPs |
|  | Solid Waste Management BMPs |
|  | Hazardous Waste Management BMPs |
|  | Contaminated Soil Management BMPs |
|  | Concrete Waste Management BMPs |
|  | Sanitary/Septic Waste Management BMPs |
|  | Liquid Waste Management BMPs |
|  | Vehicle and Equipment Cleaning BMPs |
|  | Vehicle and Equipment Fueling BMPs |
|  | Vehicle and Equipment Maintenance BMPs |
|  | Tracking Control |
|  | Stabilized Construction Entrance and Exit |
|  | Dewatering Operations BMPs |
| Erosion and Sediment Control Notes |
|  | DPP’s Construction BMP Standard Details |
|  | If any of the BMPs listed above are not included in an ESCP for a Category 4 Project, the ESCP Notes shall provide a list of the omitted BMPs with a brief explanation of why each omitted BMP is unnecessary or impracticable for the project |
| Erosion and Sediment Control Notes (continued) |
| The following inspection notes have been included under the “Project Sequence” heading: |
|  | Inspection frequency: Once every 7 days |
|  | Inspector must complete a report within 48 hours of an inspection Use DPP’s Appendix C – Construction Site BMPs Inspection Checklist for CCH Category 1A, 1B, 2, 3, and 4 and Trenching Projects Maintain all inspection reports and photographs in a “Project Log” |
| Changes to the ESCP* *for changes to the ESCP after DPP’s initial plan review |
|  | Minor changes should be noted on the site copy of the ESCP and initialed by a DPP inspector |
|  | Major changes must be proposed to the Director in writing and approved before work resumes |
| ESCP Coordinator Information |
| Designating an ESCP Coordinator: |
|  | Use DPP’s Appendix A, and have it signed by the Property Owner or Authorized Agent |
|  | A certified ESCP Coordinator must be designated with the original plan submittal; however the coordinator may be changed/updated at any time using DPP’s Appendix A or B |
|  | Changes to the ESCP Coordinator must be submitted to DPP in writing immediately for acceptance |